## Slide 1: Change BFD V0.2 Proposals
Centec Networks

## Slide 2: SAI_Change_Proposal_BFD_v0_2
Problem
  Outer header such as mac, vlan, tunnel configured in saibfd will reduce the expansibility. It need to add more attributes to support other types of BFD, such as MPLS BFD / VCCV BFD / VXLAN BFD , Micro BFD, S-BFD and so on.
Attributes | function
SAI_BFD_SESSION_ATTR_PORT | output port
SAI_BFD_SESSION_ATTR_TC | Outer L2 header
SAI_BFD_SESSION_ATTR_VLAN_TPID | Outer L2 header
SAI_BFD_SESSION_ATTR_VLAN_ID | Outer L2 header
SAI_BFD_SESSION_ATTR_VLAN_PRI | Outer L2 header
SAI_BFD_SESSION_ATTR_VLAN_CFI | Outer L2 header
SAI_BFD_SESSION_ATTR_VLAN_HEADER_VALID | Outer L2 header
SAI_BFD_SESSION_ATTR_BFD_ENCAPSULATION_TYPE | Encapsulation type
SAI_BFD_SESSION_ATTR_TUNNEL_TOS | Outer IP Tunnel header
SAI_BFD_SESSION_ATTR_TUNNEL_TTL | Outer IP Tunnel header
SAI_BFD_SESSION_ATTR_TUNNEL_SRC_IP_ADDRESS | Outer IP Tunnel header
SAI_BFD_SESSION_ATTR_TUNNEL_DST_IP_ADDRESS | Outer IP Tunnel header
SAI_BFD_SESSION_ATTR_SRC_MAC_ADDRESS | Outer L2 header
SAI_BFD_SESSION_ATTR_DST_MAC_ADDRESS | Outer L2 header

## Slide 3: SAI_Change_Proposal_BFD_v0_2
Problem
  The original format of IPinIP and L3 GRE(no RFC) in SAI
  The format of IPinIP and L3 GRE(no RFC) should be unreasonable compared with VXLAN BFD. New format refer to VXLAN(draft-ietf-bfd-vxlan-00) and classified by UDP port 3784 or 4784.
IPinIP :L2 Ethernet header | IP header | Inner IP header | Original BFD packet
L3 GRE:L2 Ethernet header | IP header | GRE header | Original BFD packet
IPinIP : L2 | IP | Inner IP | Inner UDP | BFD
GRE: L2 | IP | GRE | Inner L2 | Inner IP | Inner UDP | BFD

## Slide 4: SAI_Change_Proposal_BFD_v0_3
Solution
  Generally, the BFD session is used for monitoring a specific data traffic, so it should share the same next hop with data plane.
  Use next_hop_id to resolve the problem. The next hop including outer header format indicated by next_hop_id. So the MEPs could share the same path(nexthop) with data packet.
  It is also easier to extend to support other types of BFD.

## Slide 5: SAI_Change_Proposal_BFD_v0_3
BFD Encapsulation
It can encapsulate the BFD packet more flexible by next hop. The red header below can encapsulate by next hop.
  IP(rfc5881): L2 | IP | UDP | BFD
  MPLS(rfc5884): L2 | LSP | IP | UDP | BFD
  VXLAN(draft-ietf-bfd-vxlan-00): L2 | IP | UDP | VxLAN | Inner L2 | Inner IP | Inner UDP | BFD
  IPinIP(refer to VxLAN): L2 | IP | Inner IP | Inner UDP | BFD
  GRE(refer to VxLAN): L2 | IP | GRE | Inner L2 | Inner IP | Inner UDP | BFD
  PW VCCV(rfc5885):
  L2 | LSP | PW | ACH | BFD
  L2 | LSP | PW | ACH | IP | BFD
  L2 | Router Alert Label | PW | ACH | IP | BFD
  L2 | LSP | PW TTL=1 | ACH | IP | BFD

## Slide 6: SAI_Change_Proposal_BFD_v0_3
Add option for remote discriminator learning
Sometimes, local device does not know remote MEP’s discriminator, then need learning remote discriminator from the receiving packet

## Slide 7: SAI_Change_Proposal_BFD_v0_3
Add option for timer negotiation (P/F process)
Support timer negotiation (P/F process) in Hw offload Engine /ASIC or SW application (vendor‘s SDK or SAI)

## Slide 8: SAI_Change_Proposal_BFD_v0_3
Add some miss attributes in saibfd.h
Remove attributes in saibfd.h
attributes | flag | function
SAI_BFD_SESSION_ATTR_NEXT_HOP_ID | create and set | packet edit
SAI_BFD_SESSION_ATTR_LOCAL_DIAG | read only | local state Variables
SAI_BFD_SESSION_ATTR_REMOTE_DIAG | read only | remote State Variables
SAI_BFD_SESSION_ATTR_REMOTE_MULTIPLIER | read only | used to calculate the detection time by local system.
SAI_BFD_SESSION_ATTR_REMOTE_STATE | read only | local state Variables
SAI_BFD_SESSION_ATTR_ACTUAL_TX | read only | negotiated tx interval
SAI_BFD_SESSION_ATTR_ACTUAL_RX | read only | negotiated rx interval
SAI_BFD_SESSION_ATTR_TX_ENABLE | create and set | enable transmit BFD control packet
attributes | function
SAI_BFD_SESSION_ATTR_PORT | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_TC | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_VLAN_TPID | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_VLAN_ID | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_VLAN_PRI | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_VLAN_CFI | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_VLAN_HEADER_VALID | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_BFD_ENCAPSULATION_TYPE | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_TUNNEL_TOS | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_TUNNEL_TTL | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_TUNNEL_SRC_IP_ADDRESS | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_TUNNEL_DST_IP_ADDRESS | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_SRC_MAC_ADDRESS | replace by Nexthop ID
SAI_BFD_SESSION_ATTR_DST_MAC_ADDRESS | replace by Nexthop ID

## Slide 9: SAI_Change_Proposal_BFD_v0_3
Add attributes in saiswitch.h
attributes | Function
SAI_SWITCH_ATTR_BFD_SUPPORTED_TIMER_NEGOTIATION | indicate timer negotiation supported by switch
SAI_SWITCH_ATTR_BFD_MAX_NUMBER_OF_INTRERVALS | Max number of intervals in timer negotiation supported by switch
SAI_SWITCH_ATTR_BFD_SUPPORTED_MIN_BFD_RX_LIST | rx interval list in timer negotiation
SAI_SWITCH_ATTR_BFD_SUPPORTED_MIN_BFD_TX_LIST | tx interval list in timer negotiation

## Slide 10: SAI_Change_Proposal_BFD_v0_3
Add attributes in saihostif.h
Attributes | function
SAI_HOSTIF_TRAP_TYPE_LEARNING_BFD | Packets trapped when first BFD packet(The Your Discriminator field in received packet is 0.Received BFD packet's Your Discriminator with 0) arrive at local system.
SAI_HOSTIF_TRAP_TYPE_BFD_TIMER_NEGOTIATION | Packets trapped when received a BFD packet with P/F flag set arrive at local system.

## Slide 11: SAI_Change_Proposal_BFD_v0_3
Encapsulate the BFD packet more flexible by next hop
Add option for timer negotiation (P/F process)
Add option for remote discriminator learning
Summary

## Slide 12: Thanks!